## Slide 1
Implementation Using Cisco Packet Tracer
Intrusion Detection System (IDS)

## Slide 2
AARATHY R BABU - AM.EN.U4ECE22002
ASWATHI HS - AM.EN.U4ECE22010
HARSHIT KUMAR - AM.EN.U4ECE22017
SRUTHI BALAKRISHNAN P - AM.EN.U4ECE22046
KRISHNAPRIYA V B - AM.EN.U4ECE22052
Team Members

## Slide 3
Introduction
  Intrusion Detection System (IDS) monitors network or system activities for malicious actions or policy violations.
  Two main types:
  NIDS (Network-based IDS): Monitors network traffic.
  HIDS (Host-based IDS): Monitors individual devices or systems.
  Detects threats that bypass firewalls.
  Provides alerts for unauthorized or unusual behavior.
  Limitations:
  Cannot block attacks (unlike IPS).
  Limited performance on busy or encrypted networks.

## Slide 4
Tools and Requirements
  Software: Cisco Packet Tracer.
  Hardware:
    Intel Pentium 4 or equivalent
    2GB RAM
    1GB storage
    Standard display (1024x768)
  CLI: For device configuration.

## Slide 5
Network Design
  3 LANs with different IP ranges:
  LAN 1: 192.168.1.0/24
  LAN 2: 192.168.10.0/24
  LAN 3: 192.168.30.0/24
  Devices: PCs, laptops, printers, HTTP & FTP servers.
  Routers: Dynamic Routing between networks.

## Slide 6
Network Topology

## Slide 7
Project Implementation
  Configured devices with IPs.
  Setup routing using Dynamic Routing.
  Server configuration:
  SYSLOG for logging
  FTP (with user harsh / 123)
  HTTP (custom webpage)
  ICMP packet testing done between nodes.

## Slide 8
IDS Implementation
Network Setup
  Created 3 separate LANs using IPv4 addressing.
  Devices used: PCs, laptops, routers, switches, FTP & HTTP servers, printers.
  Configured each device with a static IP.
  Connected LANs using 3 Cisco 1941 routers with Dynamic Routing (RIP).
Service Configuration
  FTP Server: User - harsh, Password - 123
  HTTP Server: Hosted custom webpage accessible via 100.50.0.2
  SYSLOG Server: Logging service enabled for IDS alerts.
Connectivity Testing
  Ping tests performed between all networks.
  Verified file access, web access, and SYSLOG communication.

## Slide 9
Testing Network Connectivity
  After assigning IPs and configuring dynamic routing:
  Ping tests between devices in same network → Successful.
  Ping tests across networks (e.g., PC1 to PC7) → Successful after routing setup.
  HTTP Server accessed via IP 100.50.0.2 from any host.
  FTP Server tested with user credentials (harsh / 123) → Successful file access.
Testing IDS Functionality (NIDS)
  Implemented IDS on Router0 (GigabitEthernet0/0).
  Signature 2004 (ICMP Echo Request) used for detection.
  Injected ICMP packets (Ping flood) from PC7 → PC1.
  SYSLOG Server successfully logged the intrusion alerts triggered by IDS.
Experimental Results & Discussion

## Slide 10
Router Alert
Syslog Alert

## Slide 11
1. IP Address Configuration
  Manual assignment of static IP addresses across multiple devices and interfaces.
  Ensuring no IP conflicts in three separate LANs.
2. Routing Issues
  Initial routing failures between networks.
  Resolved using Dynamic Routing Protocols
3. IDS Command Complexity
  IDS setup via CLI required precise syntax and understanding of:
    Signature IDs (e.g., 2004 for ICMP Echo).
    Directory configuration for IPS.
    Logging setup and event actions.
Challenges Faced

## Slide 12
Future Scope
1. Implement Honeypot Systems
  Deploy decoy systems to lure attackers.
  Capture and study attack patterns without compromising actual resources.
  Enhances threat intelligence and improves IDS tuning.
2. Upgrade from IDS to IPS
  Transition to Intrusion Prevention System.
  Instead of just detecting and alerting, IPS can actively block malicious traffic.
  Adds a proactive security layer to the network.
3. Real-World Deployment
  Extend simulation to real network environments using real routers and switches.
  Implement in enterprise-grade setups with logging, monitoring, and alert systems.

## Slide 13
Conclusion
  Built a Network-based Intrusion Detection System (NIDS) using Cisco Packet Tracer.
  Configured and interconnected 3 separate LANs with routers and switches.
  Implemented dynamic routing and services like HTTP, FTP, and SYSLOG.
  Enabled IDS on Router0 to monitor and log ICMP Echo Request attacks using Signature 2004.

## Slide 14
THANK YOU